## Slide 1: Moving Target Defense Intrusion Detection System for IPv6 Based Advanced Metering Infrastructure
Department of Electrical Engineering
Georgia Southern University
Brycent Chatfield & Rami Haddad
Optical Networks & Smart Grid Lab.

## Slide 2: Outline
Brief overview of smart grids
Focus of study
Moving Target Defense Intrusion Detection System algorithm
Experimental overview & results
Conclusion

## Slide 3: What is a Smart Grid?
A system which includes a variety of operational and energy measures including smart meters, smart appliances, renewable energy resources, and energy efficiency resources.
Integrates high speed two-way communication technologies
  Current traditional grid features one-way communication

## Slide 4: HAN, NAN, & WAN

## Slide 5: Need for Smart Grid
Current power grid is reaching its limitation
Development of traditional power grid not keeping pace with industrial and social advancements
  Energy demands increased approximately three times within 60 year period
  Brings about challenge of using energy efficiently

## Slide 6: Vulnerabilities
Increased connectivity brings about vulnerabilities within smart grid
Consequences:
  Blackouts
  Access to personal information and energy usage
  Manipulation of pricing
  Ease of delaying, blocking, or corruption communications (DoS)
  Much larger attack surface

## Slide 7: Focus of Study
Implementation of Moving Target Defense Intrusion Detection System (MTDIDS)
  Moving Target Attacks
    New era attack vectors
    Changeable attack characteristics
    Renders conventional signature based approaches useless
Anomaly detection algorithm
  Entropy based approach
    Random routing protocol
    Planar Keys

## Slide 8: MTDIDS Overview
  Three Training Phases
    Phase 1: Random Routing Table Generation
    Phase 2: Parity Packet Rate Selection
    Phase 3: Planar Key Development
  Detection Phase
    Planar Signature Analysis
  Coordinator node/server
  Utilizes IPv6 Address Space
  Session validation timeframe

## Slide 9: Phase 1: Random Routing Table
Packet Analysis Length Parameter
  Determines size of routing table
    Randomly generated number (i.e. PAL = 1024)
  Each packet provided random IP and Port
    Packet Trajectory
    Number of IPs and Ports determined by utility company
  Rolling Window
    i.e. Transmission begins where last packet left off

## Slide 10: Phase 1: Random Routing Table
Packet Number | IPv6 Address | Port Assignment
1 | Rand(IP) | Rand(Port)
2 | Rand(IP) | Rand(Port)
3 | Rand(IP) | Rand(Port)
. | Rand(IP) | Rand(Port)
. | Rand(IP) | Rand(Port)
Packet Analysis Length | Rand(IP) | Rand(Port)

## Slide 11: Phase 2: Parity Packet Rate Selection
Parity Packet
  Packets appended with security bits
Parity Rate
  Randomly generated number
  Constitutes increment in which parity packets are selected
  i.e. PR = 3
Purpose
  Second dimension of security
  Allows detection if intruder has accessed routing table

## Slide 12: Phase 3: Planar Key Development
Secure delivery of routing table & parity information to nodes
Planar Key Creation
  Packet, IP, & Port used as coordinates
    (Packet Number,IP,Port)
  Generates signature plane for each IP
  Likewise, planar key developed for parity packets
  Valid for allotted session time

## Slide 13: Phase 3: Planar Key Development
Packet | Planar Key Coordinate
1 | Packet 1, Rand(IP), Rand(Port)
2 | Packet 2, Rand(IP), Rand(Port)
3 | Packet 3, Rand(IP), Rand(Port)
4 | Packet 4, Rand(IP), Rand(Port)
N | Packet N, Rand(IP), Rand(Port)

## Slide 14: Detection: Planar Signature Analysis
|E(Packet,IP,Port) – O(Packet,Port,IP)| = 0
Incoming packets analyzed according to packet analysis length
  Packets mapped: O(Packet,IP,Port)
  Compared to planar key: E(Packet,IP,Port)
Network Conditions
  Normal: Singularity exists at origin
  Compromised: Difference planes will populate

## Slide 15: Normal Traffic Conditions

## Slide 16: MTDIDS Experimental Overview
MATLAB used to establish TCP/IP connection
Node A and B wish to communicate
Session 1 valid for 10 minute interval
Packet Analysis Length: 25,000
Parity Rate: 3
Number of IPs: 5
Number of Ports: 65536

## Slide 17: MTDIDS Address Selection
# | IPv6 Address Selection
1 | 2001:0db8:3c4d:0015:5e39:bfc9:99b2:3ef7
2 | 2001:0db8:3c4d:0015:dab7:4ea2:d754:9943
3 | 2001:0db8:3c4d:0015:52f7:2912:96c9:e095
4 | 2001:0db8:3c4d:0015:d1a3:aaa8:99db:6ee8
5 | 2001:0db8:3c4d:0015:6185:8bac:2931:ab5e

## Slide 18: Planar Key Development

## Slide 19: Malicious Objective
Objective: Malicious node attempts to mimic network traffic to crack planar key.
Information known to attacker by means of reconnaissance:
  IPs used
  Number of ports
  Packet analysis length

## Slide 20: MTDIDS Results

## Slide 21: Conclusion
MTDIDS proposed for new era attack detection
Creates dynamic attack surface
Significantly decreases profitability of exploits
Variable Parameters
  Packet Analysis Length
  Parity Rate
  Number of IPs
  Number of Ports
  Session Time
Attack detection 4.29 times faster when implemented with solid state technology

## Slide 22: Questions