## Slide 1: Reliability and Validity of the GWalk for Use in Postural Control
Megan Mormile

## Slide 2: Reliability and Validity
Validity: The degree to which a test measures what it is supposed to measure
  Criterion: Test or assessment judged against previously established “gold standard”
  Concurrent: simultaneous collection
Reliability: Repeatability of a measure
  Intraclass Correlation Coefficient (ICC): Estimates of error variance (differences among trials)
  Test-retest method: determining stability through exact administration at multiple time points

## Slide 3: What is Postural Control?
The ability to maintain postural orientation in response to a multitude of factors (internal and external)
Integration of three main systems
Important for identification of movement patterns
  Healthy
  Pathological
Postural Control System
Visual System
Vestibular System
Somatosensory System

## Slide 4: How is Postural Control Measured?
Clinical
  BESS, Romberg, Star Excursion
  Accessible, user-friendly, subjective
  ICC values range from .50-.881
Laboratory
  Force platform, iSway
  Center of pressure: point location of vertical ground reaction force
  Expensive, requires background knowledge, objective
  ICC values typically in the excellent range: .89-.914

## Slide 5: Wireless Inertial Sensing Devices
Recent development
Previously used for gait parameters and analysis
  ICC: .83-.967
Triaxial accelerometer, gyroscope, magnetometer determine planes and axes of movement
Raw information sent via Bluetooth to computer
GWalk, Mobility Lab System, Xsens 3D, MEMS

## Slide 6: Integration of GWalk into Postural Control Analysis
Current clinical methods of balance assessment are subjective
Current methods of postural control assessment are expensive and time-consuming
GWalk may provide a portable and user-friendly measure of postural control
  Provide clinicians with objective information

## Slide 7: Purpose
To examine the test-retest reliability and criterion validity of the BTS GWalk
  Compared to COP data from force platform
  Concurrent criterion validity and test-retest reliability

## Slide 8: Research Questions
Is the GWalk a reliable and valid tool for use in postural control?
Do variables provided by the GWalk approximate those measured by ground reaction forces?

## Slide 9: Hypotheses
The GWalk will show excellent test-retest reliability across two time points
The GWalk will provide a valid measurement for assessment during static stance
  GWalk values will not significantly differ from values derived from FP

## Slide 10: Research Methods
Cross-sectional design
  Healthy collegiate cohort
Independent Variable
  Time Point 1  2
  Condition (Eyes Open (EO)/Eyes Closed (EC))
  Device
Dependent Variables
  Mediolateral/Anteroposterior Excursion (ExcML/ExcAP)

## Slide 11: Participants
56 Participants
  27 male (22 ± 1.9 years), 29 female (21 ± 0.9 years)
Recruitment from undergraduate and graduate classes within the department
  In-depth explanation of study, inclusion/exclusion criteria
Table 1. Criteria for Inclusion and Exclusion of Healthy Participants for the Current Study | 
Inclusion | Exclusion
Healthy as determined by self-report College-age (18-25 years of age) | Lower extremity musculoskeletal injury Surgery within the past year Neuromuscular injury m/TBI within past year Psychiatric illness History of seizures History of ADD/ADHD/Learning Disorder < 48 hours, >72 hours between time points

## Slide 12: Data Collection
Two time points
  48-72 hours between (52.8)
Medical history form, informed consent
Quiet standing, six trials total:
  Eyes open (3)
  Eyes closed (3)
  30 seconds

## Slide 13: Data and Statistical Analysis
Raw COP and GWalk data filtering
  Fourth order zero-phase Butterworth low-pass filter
  Cutoff frequency 12Hz
ExcML/AP calculated using custom code (MATLAB)
Reliability:
  2x2 repeated measures ANOVAs
    T1 & T2, Device
  Intraclass correlations (ICCs)
    Poor (0.0-0.39), Fair (0.40-0.59), Good (0.60-0.74), Excellent (0.75-1.0)2
Validity:
  Pearson’s correlations
    Poor (r=< .50), Moderate (r=.50-.75), Good-Excellent (r=.75-1.0)3
Alpha level: p = .05 a priori
SPSS v.23.0

## Slide 14: Results: Reliability
Repeated Measures ANOVAs (Time)
Chart: GWalk: Eyes Open
ExcAP | 0.0023 | 0.0024
ExcML | 0.0019 | 0.0019

## Slide 15
Repeated Measures ANOVAs (Time)
Chart: GWalk: Eyes Closed
ExcML | 0.0027 | 0.0027
ExcAP | 0.002 | 0.0021

## Slide 16: Results between devices statistically significant (p <.001) for all variables
Chart: ExcML: Eyes Open
| GW | FP
 | 0.0023 | 0.2489
Chart: ExcML: Eyes Closed
| GW | FP
 | 0.0027 | 0.379
Repeated Measures ANOVAs (Device)

## Slide 17: Results: Reliability
Intraclass Correlations (ICCs)
Note: ExcML= Mediolateral Excursion, ExcAP= Anteroposterior Excursion, RMSML=Mediolateral Root Mean Square, RMSAP= Anteroposterior Root Mean Square
Table 2. Intraclass Correlation Coefficient (ICC) Values for Excursion Variables in Eyes Open and Eyes Closed Quiet Standing Conditions. |  | 
Eyes Open | GWalk | Force Platform
ExcML | 0.937 | 0.904
ExcAP | 0.817 | 0.915
Eyes Closed | GWalk | Force Platform
ExcML | 0.909 | 0.936
ExcAP | 0.781 | 0.945

## Slide 18: Results: Validity
Pearson’s Correlations
Table 5. Pearson's Correlations for GWalk and Force Platform Variables |  | 
 | EO | EC
ML Exc | 0.703 | 0.722
AP Exc | 0.751 | 0.752

## Slide 19: Limitations
Location of GWalk
  Increased noise
Trial number and duration
Distractions in testing environment

## Slide 20: Conclusions
Wireless inertial sensing devices: portable yet quantifiable way to identify longer-lasting deficits
GWalk device: reliable and moderately valid device for use in postural control
  Primarily using excursion variable
Future work should aim to validate GWalk against full body marker set
Increased trial number and duration
Not recommended for use in clinical assessment at this time

## Slide 21: References
1Finnoff JT, Peterson VJ, Hollman JH, et al. Intrarater and interrater reliability of the Balance Error Scoring System (BESS). PM R. 2009;1(1): 50-4.
2Lin D, Seol H, Nussbaum MA, Madigan ML. Reliability of COP-based postural sway measures and age-related differences. Gait Posture. 2008;28(2):337-342.
3Li Z, Yan-Yi Liang, Wang L, Sheng J, Shao-Jun Ma. Reliability and validity of center of pressure measures for balance assessment in older adults. J Phys Ther Sci. 2016;28(4):1364-1367.
4Lafond D, Corriveau H, Herbert R, Prince F. Intrasession reliability of center of pressure measures of postural steadiness in healthy elderly people. Arch Phys Med Rehab. 2004;85(6):896-901.
5Sankarpandi S, Baldwin A, Ray J, Mazza C. Reliability of inertial sensors in the assessment of patients with vestibular disorders: A feasability study. BMC Ear Nose Throat Disord. 2017;17(1).
6Winter D. Human balance and posture control during standing and walking. Gait Posture. 1995;3(4):193-214
7Perpina S., Arguisuelas MD, Segura-Orti E, Montanana MT, Martinez Gramage J. Estudio de fiabilidad del sensor BTS G-Sensor durante la carrera

## Slide 22: FFT
Chart: FFT